## Slide 1: Exercise 1
Write a program that given n of a value between 1 and 26, prints the following:
A1 A2 A3 … An
int n;
printf(“Enter n between 1 and 26:\n”);
scanf(“%d”, &n);
for (int index = 1; index <=n; index++){
printf(“A%d ”, index);
}

## Slide 2: Exercise 2
Write a program that given n of a value between 1 and 26, and a character X prints the following:
X1 X2 X3 … Xn
int n;
char c;
printf(“Enter a number and a letter:\n”);
scanf(“%d %c”, &n, &c);
for (int index = 1; index <=n; index++){
printf(“%c%d ”, c, index);
}

## Slide 3: Exercise 3
Write a program that given n of a value between 1 and 26, prints the following table:
A1 A2 A3 … An
B1 B2 B3 … Bn
…
?1 ?2 ?3 … ?n
where ‘?’ is the nth letter of the alphabet.
n = 2
A1 A2
B1 B2
n = 3
A1 A2 A3
B1 B2 B3
C1 C2 C3

## Slide 4: Exercise 3: Algorithm Design
Read number n from user;
Validate: make sure n between 1 and 26
If n >= 1: print row ‘1’ for A1 to An
If n >= 2: print row ‘2’ for B1 to Bn, else exit
… … …
If n >= idx: print row ‘idx’ for Ridx1 to Ridxn, else exit
… … …
Print row n for ?1 to ?n, exit

## Slide 5: Exercise 3: Steps using a loop
Read number n from user;
Validate: make sure number is between 1 and 26
int idx;
for (idx = 1; idx <=n; idx++) {
print row idx;
}

## Slide 6: Exercise 3: Expand the row
Read number n from user;
Validate
int idx;
for (idx = 1; idx <=n; idx++) {
//print row idx;
print “?1 “
print “?2 “
…
print “?n \n”
}

## Slide 7: Exercise 3: Row as an insider loop
Read number n from user;
Validate
int idx;
for (idx = 1; idx <=n; idx++) {
for (idx2 = 1; idx2 <= n; idx2++) {
print “?idx2 ”
}
}
//Should know replacement for ‘?’

## Slide 8: Exercise 3: Represent the letter
Read number n from user;
Validate
int idx; char letter = ‘A’;
for (idx = 1; idx <=n; idx++) {
for (idx2 = 1; idx2 <= n; idx2++) {
print letter idx2
}
letter++;
}
//Should know replacement for ‘?’

## Slide 9: Exercise 3: Move letter to outer for
Read number n from user;
Validate
int idx, idx2; char letter = ‘A’;
for (idx = 1; idx <=n; idx++,letter++) {
for (idx2 = 1; idx2 <= n; idx2++) {
print letter idx
}
//letter++;
}
//Should know replacement for ‘?’

## Slide 10: Exercise 3: Solution: Use Nested Loops
int n, idx, idx2;
char letter = ‘A’;
//Read input
printf(“Enter n: (1..26)\n”);
scanf(“%d”, &n);
//Validate
if (n < 1 || n > 26) {
printf(“Not a valid nb.\n”);
return 1;
}
//Print table
for (idx = 1; idx<=n; idx++,letter++) {
for (idx2 = 1; idx2 <= n; idx2++) {
printf (“%c%d “, letter, idx2);
}
printf(“\n”);
}
return 0;

## Slide 11: Exercise 4
Write a program to print out the following pattern consisting of x rows where x is an integer read from standard input:
!
!!
!!!
!!!!
!!!!!
!!!!!!

## Slide 12: Exercise 4
Write a program to print out the following pattern consisting of x rows where x is an integer read from standard input:
! Row 1: 1 ex. mark
!! Row 2: 2 ex. marks
!!! …
!!!! Row x: x ex. marks
!!!!! …
!!!!!!

## Slide 13: Exercise 4: Solution: Use Nested Loops
Write a program to print out the following pattern consisting of x rows where x is an integer read from standard input:
for (idx1 = 1; idx1<=n; idx1++) {
for (idx2 = 1; idx2 <= idx1; idx2++) {
printf (“!“);
}
printf(“\n”);
}

## Slide 14: Quiz 07
How many characters does the inner loop print for line i, i=1, 2, … n?
for (idx1 = 1; idx1<=n; idx1++) {
for (idx2 = 1; idx2 <= idx1; idx2++) {
printf (“!“);
}
printf(“\n”);
}

## Slide 15: Summary
Iteration statements
  While loop
  Do loop
  For loop
break, continue
Comma operator
Null statement
Nested loops

## Slide 16: CSE 220 – C Programming Lecture 11
Data Types

## Slide 17: Basic Types
Integer types
Floating types
Character types
Type conversion
Type definition

## Slide 18: Integer Types (I)
Whole numbers
Signed/Unsigned
  Signed: most significant bit denotes the sign: 1 if – 0 if +
  By default, integers are signed
Length (machine dependent):
  int: 16/32bits
  long int, long: 32/64bits
  short int, short: 16bits
sizeof operator: number of bytes:
  sizeof(char): 1 sizeof(int): 4 sizeof(long): 8
long int ³ int ³ short int

## Slide 19: Integer Types (II)
111111111 00101000 00111000 00000110
  signed int x: - (230 + 229 + ….)
  unsigned int x: +231 + …
Integer overflow (16-bit case):
  Signed: 0111111111111111 + 0000000000000001
  Result does not fit in 16 bits
  If signed: behavior undefined
  If unsigned: correct answer modulo 2n Namely discard the overflown bits
0
30
31

## Slide 20: Integer Constants
C allows constants to be written in:
  Decimal: base 10
    Digits between 0 and 9, must not begin with 0
    34 199
  Octal: base 8
    Digits between 0 and 7, must begin with 0
    034 07777
  Hexadecimal: base 16
    Digits: need 15: 0,1,2,3,4,5,6,7,8,9,a,b,c,d,e,f
    must begin with 0x
    0xFA 0X2fCB 0xfddd 0xfddd
long
unsigned
L
U

## Slide 21: Floating Types
float: single precision (32bits, 6 digits)
double: double precision (64 bits, 15 digits)
long double: extended precision
Float Bits: 1 0 ----- 0 1 ------------- 1
  Sign (1)
  Exponent (8)
  Fraction (23)

## Slide 22: Floating Constants
Contain a decimal point and/or exponent:
  36.0 36. .36e2 36E0 360e-1
By default: stored as double
To force as float:
  360.0f
To force as double:
  360.0l